Dynamips & Gxemul 初步分析
Valpassing

---
演示
一个简单的dynamips仿真router和网络

---
Dynamips
1. 硬件架构模拟平台，CPU:MIPS64, PPC64
2. 板卡模拟：NS16552 DUART, Dallas DS1216 chip(NVRAM),
 * Cisco 7200 I/O FPGA:
 * - Simulates a NMC93C46 Serial EEPROM as CPU and Midplane EEPROM.
 * - Simulates a DALLAS DS1620 for Temperature Sensors.
 * - Simulates voltage sensors.
 * - Simulates console and AUX ports (SCN2681).
DECchip 21140 PCI fast Ethernet LAN controller
AMD Am79c971 FastEthernet chip emulation
3. 虚拟网络模拟: frame_relay, eth_switch
4. 与Hypervisor和tty交互

---
Dynamips's SW结构 from dynamips.c
#include "dynamips.h"
#include "cpu.h"
#include "mips64_exec.h"
#include "mips64_jit.h"
#include "ppc32_exec.h"
#include "ppc32_jit.h"
#include "dev_c7200.h"
#include "dev_c3600.h"
#include "dev_c2691.h"
#include "dev_c3725.h"
#include "dev_c3745.h"
#include "dev_c2600.h"
#include "dev_msfc1.h"
#include "ppc32_vmtest.h"
#include "dev_vtty.h"
#include "ptask.h"
#include "timer.h"
#include "registry.h"
#include "hypervisor.h"
#include "net_io.h"
#include "net_io_bridge.h"
#include "net_io_filter.h"
#include "crc.h"
#include "atm.h"
#include "frame_relay.h"
#include "eth_switch.h"

---
Dynamips的router模拟结构
CPU
VM
PC, gpr
dev_array
Dev
cpu_mips_t
cpu_gen_t

---
Dynamips –MIPS架构模拟 1
1. MIPS的寄存器：
/* MIPS general purpose registers names */
char *mips64_gpr_reg_names[MIPS64_GPR_NR] = {
   "zr", "at", "v0", "v1", "a0", "a1", "a2", "a3",
   "t0", "t1", "t2", "t3", "t4", "t5", "t6", "t7",
   "s0", "s1", "s2", "s3", "s4", "s5", "s6", "s7",
   "t8", "t9", "k0", "k1", "gp", "sp", "fp", "ra",
};
在mips64.h中可以看到所有regiester的定义，包括gpr和cp0的register

---
Dynamips –MIPS架构模拟 2
1. 指令：
static struct mips64_insn_exec_tag mips64_exec_tags[] = {
   { "add" , mips64_exec_ADD , 0xfc0007ff , 0x00000020, 1, 3 },
   { "j" , mips64_exec_J , 0xfc000000 , 0x08000000, 0, 11 },
2. 在mips64_exec_J中，cpu->pc = new_pc;
3. 在mips64_exec_ADD中，
/* ADD */
static fastcall int mips64_exec_ADD(cpu_mips_t *cpu,mips_insn_t insn)
{
   int rs = bits(insn,21,25);
   int rt = bits(insn,16,20);
   int rd = bits(insn,11,15);
   /* TODO: Exception handling */
   res = (m_uint32_t)cpu->gpr[rs] + (m_uint32_t)cpu->gpr[rt];
   cpu->gpr[rd] = sign_extend(res,32);
   return(0);

---
Dynamips –Memory OP 1
1. LW 操作
/* LW (Load Word) */
static fastcall int mips64_exec_LW(cpu_mips_t *cpu,mips_insn_t insn)
{
   int base = bits(insn,21,25);
   int rt = bits(insn,16,20);
   int offset = bits(insn,0,15);
return(mips64_exec_memop2(cpu,MIPS_MEMOP_LW,base,offset,rt,TRUE));
}
最后调用了MTS_PROTO(access)
2. Sw操作
/* SW (Store Word) */
static fastcall int mips64_exec_SW(cpu_mips_t *cpu,mips_insn_t insn)
{
   int base = bits(insn,21,25);
   int rt = bits(insn,16,20);
   int offset = bits(insn,0,15);
   return(mips64_exec_memop2(cpu,MIPS_MEMOP_SW,base,offset,rt,FALSE));
}
最后调用了MTS_PROTO(access)

---
Dynamips –Memory OP 2
MTS_PROTO(access)，以mips64_mts64_access为例
void *mips64_mts64_access(cpu_mips_t *cpu,m_uint64_t vaddr,
        u_int op_code,u_int op_size,
        u_int op_type,m_uint64_t *data,
        u_int *exc)
给出的是virtual address，首先要转成physical address，然后根据具体的地址访问区分
cache
memory
IO -- 每个device在注册到系统中的时候都给出一个它的地址范围

---
Dynamips –Memory DEV操作
从access中调用
dev_access_fast(cpu->gen,dev_id,haddr,op_size,op_type,data)
取得dev_id对应的vdevice结构
struct vdevice *dev = cpu->vm->dev_array[dev_id];
调用device的handler
dev->handler(cpu,dev,offset,op_size,op_type,data)
handler的注册：在每一个dev（chip/controller）初始化的时候用dev_create生成一个vdevice结构，并赋值handler

---
Dynamips –TTY
CMD
vtty_thread
vm
set_irq
Tcp port
vtty
Vtty
vtty_list

---
Gxemul
settings
emul
Machines
Machine
diskimage
x11-md
memory
Cpu
cpu-family
fb_data / fb_windows
memory_devices

---
DEVINIT
分配一个memory_device结构，然后关联memory和memory_device
与dynamips非常类似
注册memory的访问地址
注册dev_xxx_access函数